Adding IPv4 address space

---
Intro to arpanet
- Arpanet was divided into 254 networks
- 0
- IPv4 was an address extension: 0->0.0.0.0

---
0.0.0.0/8
- 0.0.0.0 is special
- 0.0.0.0/8 was “This” network.
  - Subsumed by public IPv4 addresses
  - Later subsumed by RFC1918
- Last arpanet node retired February 28, 1990.
- No use for 0 since!

---
.0 as broadcast
Ping -b

---
There’s a patch for this

---
127.0.0.0/8
- Host-local
  - Unix domain sockets
- We’ve seen 127.0.1.X – but nothing else
- Why use up a whole /8?
  - Cutting it down to a /16 frees up 16m addresses
- Problems:
  - Hard coded configuration in /etc/hosts, conf files

---
232.0.0.0-239.0.0.0

---
232.0.0.0-239.0.0.0 Problems

---
Other source code bases
- IOT
  - Zephyr – one patch
  - RIOTos – 6lowpan based, no problems
  - FreeRTOS -
- DDPK – one patch
- VP.IO
- Windows

---
Bootloaders & BIOSes

---
Routing daemons
- Despite the presence of 224/3 or 240/4 etc in all the major bogon lists, it turned out
- This was the patch (for 240 only) for babel
- Bird

---
240.0.0.0/4 (class-e)

---
DNS
- Reverse lookups for 0, 127, & 255 are trapped by debian9 and not sent to the roots.
  - Bind 9 just traps 255.255.255.255 as it should
- 224/4 is sent to the roots
- 240/4 is sent to the roots
- So all we need to do is fix 0 and 127...
  - We’ve got a patch for that...

---
Summary
Range	Exclude	Total IP addresses
0.0.0.0/8	0.0.0.0/32	16,777,215
127.0.0.0/8	127.0.0.0/16	16,777,216
224.0.0.0/8	224-231, 238-239	117440512
240.0.0.0/8	255.255.255.255/32	268,435,455
	Total	419,364,864